## Slide 1: Mini oscilloscope
Pwm signal drawer
Using :
1- ATMega32 Microcontroller
2- GLCD
AMIT Graduation Project
Presented by : Yassein Hamed
D53 online
yasseinhamed67@outlook.sa

## Slide 2: Specification
❑ With the graphical LCD we can display the following:
• The shape of the generated PWM from externally
sources.
• The frequency in KHz of the generated wave .
• The duty cycle of the generated wave .
• The time of the single cycle.

## Slide 3: Layered architecture
1- Application Layer
App.h
2- Hardware Abstraction Layer
GLCD.h
3- Microcontroller Abstraction Layer
DIO.h PWM.h ICU.h

## Slide 4: flowchart
Initialization
Measure Signal
Draw Signal

## Slide 5: Measure Signal
Clear Input Capture Flag Set
Trigger Edge: RISING_EDG
Wait for Input Capture →
Set value to A
Clear Input Capture Flag Set
Trigger Edge: RISING_EDGE
Wait for Input Capture →
Set value to B
Clear Input Capture Flag Set
Trigger Edge: Falling_EDGE
Wait for Input Capture →
Set value to c
Period time = B-A
high Time = C-B
Duty = Ton / T ;
ICU_GetSignal();

## Slide 6: Draw Signal
Draw_Signal();
GLCD_DisplayString();
Get duty cycle from ICU
GLCD Line 0: Display Frequency
Value in kHz
GLCD Line 0: Display Duty Cycle
Value in %.
GLCD Line 4: Display Period Time
Value in milliseconds.
GLCD Line 6: Display Arrow on
First Cycle Period Time
GLCD Line 7: Display the PWM
signal shape
repeat

## Slide 7
Start
Initialization
Get signal
Draw time arrow
loop
sync
End
continue
stop